## Slide 1
Main Models -QoS
500
There are three main models for providing QoS services in a network:
Best Effort, Integrated Services (IntServ), Differentiated Services (DiffServ).
The three models are differentiated by how each one enables applications to send data and the way the network handles data delivery within a specified level of service.
Best Effort :
The Best Effort (BE) QoS model is the simplest of the three. It is the default QoS model used for Internet and it doesn’t implement any QoS mechanism at all, that is the reason why there isn’t any complexity associated to this QoS model.
BE does not allow for resource reservation or any other mechanism related to asking for some kind of special treatment to the network. For this reason, BE model does not work very well will any emerging application with real-time (RT) traffic demands.
This model should not be used when the network resources are not enough to fulfill the QoS application requirements in terms of the main indicators as bandwidth, delay, jitter, etc. In these cases, with applications competing for resources, the quality of the end-user experience could be very poor if there is no other mechanism in place to manage the unfairness.

## Slide 2
Differentiated Services
500
Differentiated Services (DiffServ) is a framework used in computer and telecommunication networks to provide quality of service (QoS) on a per-flow basis.
Objective: DiffServ aims to improve network performance and control by categorizing network traffic into different classes or levels of service. This allows network administrators to manage traffic more effectively based on priorities and requirements.
Traffic Classification: Traffic entering a DiffServ-enabled network is classified into different classes or behaviors. These classes are typically defined based on criteria such as application type, source/destination address, or protocol.
Per-Hop-Behavior (PHB): DiffServ defines several different types of per-hop behaviors, which dictate how traffic in each class should be treated as it travels through a network. For example, some traffic may be given expedited forwarding with minimal delay and loss, while other traffic may be given best-effort forwarding.
Differentiated Treatment: Once traffic is classified and assigned a per-hop behavior, routers and switches along the path can prioritize and forward packets accordingly. This allows for differentiated treatment of traffic based on its class, ensuring that higher-priority traffic receives better service levels.
Scalability and Simplicity: DiffServ is designed to be scalable and easy to implement compared to older QoS models like Integrated Services (IntServ). By focusing on aggregate traffic classes rather than individual flows, DiffServ reduces the complexity of QoS management in large-scale networks.
Deployment: DiffServ is commonly implemented in enterprise networks, Internet service provider (ISP) networks, and other large-scale networks where QoS management is crucial for maintaining performance levels and meeting service level agreements (SLAs).

## Slide 3
Differentiated Services
Call-based and flow-based QoS are two approaches to managing Quality of Service (QoS) in networks, each with its own characteristics and applications:
Call-Based QoS:
  Definition: Call-based QoS, also known as connection-oriented QoS, focuses on providing QoS guarantees for individual network sessions or calls.
  Usage: It is commonly used in circuit-switched networks and in VoIP (Voice over IP) systems where each call requires specific bandwidth, latency, and reliability guarantees.
  Characteristics:
    Resources are reserved for each call or session at the time of setup.
    Guarantees can include specific levels of bandwidth, delay, jitter, and packet loss.
    Typically involves signaling protocols (e.g., RSVP - Resource Reservation Protocol) to establish and maintain QoS parameters for each session.
    QoS policies are applied to traffic flows rather than to individual packets or sessions.
    Does not require explicit reservation of resources; instead, it uses mechanisms like DiffServ (Differentiated Services) to mark packets and prioritize them accordingly.
500

## Slide 4
Differentiated Services
Flow-Based QoS:
  Definition: Flow-based QoS, also known as connectionless QoS, focuses on managing QoS based on aggregated traffic flows rather than individual sessions.
  Usage: It is widely used in IP-based networks (like the Internet) where individual flows (streams of packets) are dynamically handled based on their QoS requirements.
  Characteristics:
    Traffic is classified into different flows based on criteria such as source/destination IP addresses, port numbers, or protocol types.
    QoS policies are applied to traffic flows rather than to individual packets or sessions.
    Does not require explicit reservation of resources; instead, it uses mechanisms like DiffServ (Differentiated Services) to mark packets and prioritize them accordingly.
500

## Slide 5
Differentiated Services-Expedited Traffic
500
Expedited Forwarding (EF) is a Per-Hop Behavior (PHB) defined within the Differentiated Services (DiffServ) framework. It is used to provide a low-loss, low-latency, and low-jitter forwarding treatment for certain classes of traffic that require assured quality of service.
Purpose:
  EF is designed for real-time, delay-sensitive traffic such as voice (VoIP) and video conferencing.
  It ensures that packets belonging to an EF class receive preferential treatment through the network.
Traffic Characteristics:
  EF typically handles traffic with strict QoS requirements that cannot tolerate delays or packet loss beyond certain thresholds.
  Examples include real-time applications where maintaining a consistent and predictable quality of service is critical.
Behavior:
  EF provides a single, well-defined behavior for packets in the EF class across the network.
  Routers and switches implementing EF prioritize these packets over other traffic, ensuring minimal delay, jitter, and loss.

## Slide 6
Differentiated Services-Expedited Traffic
500
Implementation:
  EF is implemented by marking packets with a specific DiffServ Code Point (DSCP) value in the IP header.
  The DSCP value associated with EF is usually 46 (decimal) or 101110 (binary), which indicates Expedited Forwarding with a high-priority treatment.
Network Considerations:
  Networks must be properly configured to support EF, including ensuring sufficient bandwidth and minimal queuing delays for EF traffic.
  Traffic engineering and network design considerations are important to maintain EF performance across the entire network path.
Compatibility:
  EF can coexist with other DiffServ behaviors such as Assured Forwarding (AF), allowing different traffic classes to receive appropriate QoS treatments based on their needs.

## Slide 7
Differentiated Services
500

## Slide 8
Differentiated Services-Regular Trafic
500
Regular traffic refers to the general data traffic that flows through a network without requiring specialized Quality of Service (QoS) treatment such as Expedited Forwarding (EF) or other prioritization schemes.
Characteristics:
  Best-Effort Delivery: Regular traffic is typically handled using a best-effort delivery model, where packets are forwarded on a first-come, first-served basis without any guarantees regarding latency, jitter, or packet loss.
  Variable QoS: It may experience varying levels of QoS depending on network congestion, available bandwidth, and the network's overall load at any given time.
  Typical Applications: Examples of regular traffic include web browsing, email, file downloads, and non-real-time data transfers that do not require immediate or guaranteed delivery.
Handling in Networks:
  DiffServ and Class of Service (CoS): In networks that implement DiffServ, regular traffic might be assigned to a default or lower-priority class of service compared to more critical traffic types like voice or video.
  Queuing and Congestion Management: Routers and switches may use various queuing and congestion management mechanisms (e.g., FIFO, Tail Drop) for regular traffic to ensure fair sharing of network resources among all users.

## Slide 9
Differentiated Services-RegularTraffic
500
QoS Considerations:
Impact of Congestion: During periods of network congestion, regular traffic may experience increased latency or packet loss as resources are prioritized for higher-priority traffic classes.
Service Level Agreements (SLAs): Businesses and service providers may define SLAs that specify the acceptable QoS levels for regular traffic, ensuring that it meets minimum performance standards even under load.
Implementation:
DSCP Marking: Regular traffic is often marked with a standard DSCP value (e.g., 0 or 1) to indicate best-effort forwarding treatment within the DiffServ framework.
Traffic Engineering: Network administrators may perform traffic engineering to optimize regular traffic flow and mitigate congestion impacts through techniques like load balancing and route optimization.

## Slide 10
Differentiated Services-Assured Forwarding
500

## Slide 11
Differentiated Services-Assured Forwarding
500
Assured Forwarding (AF) is another Per-Hop Behavior (PHB) defined within the Differentiated Services (DiffServ) framework. It is designed to provide different levels of forwarding assurances and prioritization for various classes of traffic based on their QoS requirements.
Purpose:
  Assured Forwarding is intended to provide predictable and differentiated levels of QoS for different classes of traffic.
  It ensures that packets belonging to certain traffic classes receive a specified level of forwarding assurance, which helps in managing network resources and meeting application requirements.
Traffic Classes:
  AF defines four different classes or queues, often referred to as AF1, AF2, AF3, and AF4.
  Each AF class provides a different level of assurance in terms of packet drop probability and delay sensitivity.
Behavior:
  Drop Probability: AF classes are defined with different drop probabilities under network congestion. For example, AF1 has a higher drop probability compared to AF4.
  Prioritization: Within each AF class, packets may be further prioritized based on their marking (e.g., within AF1, AF11 might have higher priority than AF12).

## Slide 12
Differentiated Services-Assured Forwarding
500
Implementation:
  AF is implemented by marking packets with a specific DSCP (Differentiated Services Code Point) value in the IP header.
  The DSCP values associated with AF are typically 10, 12, 14, and 18 (binary: 001010, 001100, 001110, and 010010 respectively), corresponding to AF1, AF2, AF3, and AF4.
Network Management:
  AF allows network administrators to allocate resources and manage congestion more effectively by classifying traffic into different AF classes.
  It supports better handling of applications with varying QoS requirements, such as business-critical data, video streaming, or bulk data transfers.
Compatibility:
  AF can coexist with other DiffServ PHBs, allowing for a flexible and scalable approach to QoS management within networks.
In summary, Assured Forwarding (AF) is a QoS mechanism in DiffServ that provides different levels of assurance for forwarding packets based on their class, enabling more predictable performance for applications with specific QoS requirements.
It strikes a balance between providing differentiated treatment for traffic classes while simplifying network management compared to more complex QoS mechanisms like Expedited Forwarding (EF).

## Slide 13
Integrated Services-Benefits and Limitations
500
IntServ Benefits:
Good solution for managing flows in small networks.
Intserv enables hosts to request per-ﬂow, quantiﬁable resources, along end-to-end data paths and to obtain feedback regarding admissibility of these requests.
IntServ Limitations:
Poor scalability.
High resource consumption on the network nodes.
  Per flow processing (CPU): signaling & processing load.
  Per flow state (memory): to keep track of every flow traversing the node.
  Continuous signaling (RSVP is a soft state protocol).
It’s very difficult to implement.

## Slide 14
Differentiated Services-Benefits and Limitations
500
DiffServ Benefits:
Highly scalable QoS mechanism.
Does not require any resource reservation mechanism on end hosts.
Easy configuration, operation and maintenance.
Support complex traffic classification and conditioning at the edge.
Can aggregate multiple app flows into a limited number of TCs.
Reduced overhead associated to the maintenance of policies on a per flow basis.
Diffserv nodes can process traffic more easily than Intserv devices.
Diffserv is a distributed QoS service model. Resource allocation is distributed among all the routers of a Diffserv domain, allowing for a greater flexibility and efficiency in the routing process.
DiffServ Limitaions:
Coordination between domains in the QoS end-to-end service.
SPs QoS customization may affect the guaranteed QoS end-to-end service.