## Slide 1: Basic Structures of Computers
COMPUTER ORGANIZATION
Course Code: 16CS35

## Slide 2
Functional units
Basic Operational Concepts
Bus Structures
Performance
    Processor clock
    Basic performance equation
    Pipelining and Superscalar operation
    Clock rate
    Performance measurement- SPEC, CISC and RISC models.

## Slide 3
Difference between Computer organization and Computer architecture
Computer organization
Deals with all physical components of computer systems that interacts with each other to perform various functionalities
The lower level of computer organization is known as micro-architecture which is more detailed and concrete.
Examples of Organizational attributes includes Hardware details transparent to the programmer such as control signal and peripheral.

## Slide 4
Definition of Computer:
A Digital computer is a fast electronic calculating machine that accepts digitized input information, processes it according to a list of internally stored instructions and produces the resulting output information.
List of Instructions: is called a computer program
Internally stored: Program that is stored in memory.
Data: Data are numbers and encoded characters that are used as operands by the instructions.

## Slide 5
Functional units
Basic Functional units of a computer are:
Input Unit
Output Unit
Memory
Arithmetic Unit
Control Unit
Program
&
Data
Control Unit
Input Unit
Output
Unit
Memory
Arithmetic
Logic Unit
Central
Processing
Unit
Result

## Slide 6
Input Unit
Computer accept coded information through input units, which read the data. Some of the devices are –
  Keyboard
  joysticks
  trackballs
  mouse
  Audio input through Microphones

## Slide 7
Memory Unit
The function of memory unit is to store programs and data.
Memory is classified based on three factors –
  Speed
  Cost
  Size
  The figure shows the hierarchy of memory -

## Slide 8
Memory Speed, Cost and Size
Processor
Primary Cache
Secondary cache
Magnetic disk
Main
memory
Increasing
size
speed
memory
cost per bit
Registers
L1
L2
Increasing
Increasing

## Slide 9
Arithmetic Logic Unit (ALU)
Most computer operations are executed in the arithmetic and logic unit (ALU)
The arithmetic operations are performed by bringing the operands from the memory or I/O device into fast registers of the processor, from where the operands are moved to the ALU to perform the required operation.
Registers can store one word and are much faster than the cache memory.
Output Unit:
Output unit function is to send processed results to the outside world. Some of the devices are – monitor, printer etc.

## Slide 10
Control Unit
Control unit is the nerve center that sends control signals to other units and senses their states. The signals sent are –
  The actual timing signals that govern the transfers are generated.
  Data transfers between the processor and the memory are controlled.
  Data transfers between the processor and I/O are controlled.
  Program fetch and decoding is controlled.

## Slide 11
Operation of a computer
The computer accepts information in the form of programs and data through an input unit and stores it in the memory.
Information stored in the memory is fetched, under program control, into an execution unit (which has ALU), where the data is processed.
The processed information leaves the computer through an output unit.
All activities inside the machine are directed by the control unit.

## Slide 12: Review
Activity in a computer is governed by instructions.
To perform a task, an appropriate program consisting of a list of instructions is stored in the memory.
Individual instructions are brought from the memory into the processor, which executes the specified operations.
Data to be used as operands are also stored in the memory.

## Slide 13
Data Storage and Addressing
Numbers and character operands, as well as instructions are stored in the memory of a computer.
The memory is organized so that a group of n bits can be stored or retrieved in a single, basic operation. Each group of n bits is referred to as a word of information and n is called the word length. n bits
First word
Second word

## Slide 14
There are two ways that byte addresses can be assigned across words.
Big-endian assignment
Little-endian assignment.
Word Byte Address Byte Address
Add
Big-endian assignment Little-endian assignment
Byte and word addressing
0 | 0 | 1 | 2 | 3
4 | 4 | 5 | 6 | 7
 | : |  |  | 
22-4 | 2k-4 | 2k-3 | 2k-2 | 2k-1
0 | 3 | 2 | 1 | 0
4 | 7 | 6 | 5 | 4
 | : |  |  | 
22-4 | 2k-1 | 2k-2 | 2k-3 | 2k-4

## Slide 15: A Typical Instruction
Add LOCA, R0
Add the operand at memory location LOCA to the operand in a register R0 in the processor.
Place the sum into register R0.
The original contents of LOCA are preserved.
The original contents of R0 is overwritten.
Instruction is fetched from the memory into the processor – the operand at LOCA is fetched and added to the contents of R0 – the resulting sum is stored in register R0.

## Slide 16: Separate Memory Access and ALU Operation
Load LOCA, R1
Add R1, R0
Whose contents will be overwritten?
The contents of R0 is overwritten.
Explanation: Here the data from memory location LOCA is brought to R1.
The contents of R1 is added to R0.
The result is stored back into to R0. (Note: The old contents of R0 is replaced by the sum in R0)

## Slide 17: Connection Between the Processor and the Memory
Connections between the processor and the memory.
Processor
Memory
PC
IR
MDR
Control
ALU
R0
MAR
n general purpose registers
R1
Rn-1

## Slide 18: Registers
Instruction register (IR)
Program counter (PC)
General-purpose register (R0 – Rn-1)
Memory address register (MAR)
Memory data register (MDR)

## Slide 19: Typical Operating Steps
Programs reside in the memory through input devices
PC is set to point to the first instruction
The contents of PC are transferred to MAR
A Read signal is sent to the memory
The first instruction is read out and loaded into MDR
The contents of MDR are transferred to IR
Decode and execute the instruction

## Slide 20: Typical Operating Steps (Cont’)
Get operands for ALU
  General-purpose register
  Memory (address to MAR – Read – MDR to ALU)
Perform operation in ALU
Store the result back
  To general-purpose register
  To memory (address to MAR, result to MDR – Write)
During the execution, PC is incremented to the next instruction

## Slide 21: Interrupt
Normal execution of programs may be preempted if some device requires urgent servicing.
The normal execution of the current program must be interrupted – the device raises an interrupt signal.
Interrupt-service routine is executed
Current system information backup and restore (PC, general-purpose registers, control information, specific information)

## Slide 22: Bus Structures
There are many ways to connect different parts inside a computer together.
A group of lines that serves as a connecting path for several devices is called a bus.
The different busses in a system are
    Address
    Data
    Control

## Slide 23: Bus Structure
Single-bus
. Single-bus structure.
Memory
Input
Output
Processor

## Slide 24
CPU
Memory
Memory
I/O
I/O
…
…
Control
Address
Data
Bus Structure

## Slide 25: Speed Issue
Different devices have different transfer/ operate speed.
If the speed of bus is bounded by the slowest device connected to it, the efficiency will be very low.
How to solve this?
A common approach – use buffers.

## Slide 26: Performance
The most important measure of a computer is how quickly it can execute programs.
Three factors affect performance:
Hardware design
Instruction set
Compiler

## Slide 27: Performance
Processor time to execute a program depends on the hardware involved in the execution of individual machine instructions.
Main
memory
Processor
Bus
Cache
memory
Figure 1.5.
The processor cache.

## Slide 28: Performance
The processor and a relatively small cache memory can be fabricated on a single integrated circuit chip.
Speed
Cost
Memory management

## Slide 29: Processor Clock
Clock, clock cycle, and clock rate
  Clock is the timing signal of a processor
  Clock cycle is the regular time interval of a clock
  Clock rate is the number of clock cycles per second.
    Cycles per second is called herts (Hz).
    Mega herts is Million instructions per second. (M Hz)
    Giga herts is Billion instructions per second. (GHz)
The execution of each instruction is divided into several steps, each of which completes in one clock cycle.

## Slide 30: Basic Performance Equation
T – processor time required to execute a program that has been prepared in high-level language
N – number of actual machine language instructions needed to complete the execution (note: loop)
S – average number of basic steps needed to execute one machine instruction. Each step completes in one clock cycle
R – clock rate
Note: these are not independent to each other
How to improve T?

## Slide 31: Pipeline and Superscalar Operation
Instructions are not necessarily executed one after another.
The value of S doesn’t have to be the number of clock cycles to execute one instruction.
Pipelining – overlapping the execution of successive instructions.
Add R1, R2, R3
Superscalar operation – multiple instruction pipelines are implemented in the processor.
Goal – reduce S (could become <1!)

## Slide 32: Clock Rate
Increase clock rate
Improve the integrated-circuit (IC) technology to make the circuits faster
Reduce the amount of processing done in one basic step (however, this may increase the number of basic steps needed)
Increases in R that are entirely caused by improvements in IC technology affect all aspects of the processor’s operation equally except the time to access the main memory.

## Slide 33: CISC and RISC
Tradeoff between N and S
A key consideration is the use of pipelining
S is close to 1 even though the number of basic steps per instruction may be considerably larger
It is much easier to implement efficient pipelining in processor with simple instruction sets
Reduced Instruction Set Computers (RISC)
Complex Instruction Set Computers (CISC)

## Slide 34: Compiler
A compiler translates a high-level language program into a sequence of machine instructions.
To reduce N, we need a suitable machine instruction set and a compiler that makes good use of it.
Goal – reduce N×S
A compiler may not be designed for a specific processor; however, a high-quality compiler is usually designed for, and with, a specific processor.

## Slide 35: Performance Measurement
T is difficult to compute.
Measure computer performance using benchmark programs.
System Performance Evaluation Corporation (SPEC) selects and publishes representative application programs for different application domains, together with test results for many commercially available computers.
Compile and run (no simulation)
Reference computer

## Slide 36
Where n is the number of programs in the suite.

## Slide 38
Questions:
What is the basic difference between Computer Organization and Computer Architecture.
Write the functional block of a computer and explain briefly each part.
Write the functional blocks of a computer and explain the operation of a computer.
What are the factor on which the memory devices are classified? Explain.
Explain the characteristics of memory devices with reference to memory hierarchy.
What are the basic signals used by the control unit? What is it used for?
What are the different byte addresses that can be assigned across words?
Show how byte and word addressing is assigned?

## Slide 39
List the steps needed to execute the machine instruction
Add LocA, R0
Assume that instruction itself is stored in the memory location INSTR and that this address is initially in PC register. Assume MAR, MDR, PC, IR, R0-R7 and ALU are available in the processor.
Repeat the problem 8 for the instruction
Add R1, R2, R3
What is an interrupt?
What is Interrupt Service Routine?
What is the procedure adopted by a processor when there is an interrupt?
What is a Bus? What are the different types of busses in a system?
What is the advantage and disadvantage of a bus system?
What are the factors that affect the performance of a system?
What is the difference between CISC and RISC processor?